## Slide 1: Impedance Control Cable-Driven Gripper
James Quek
Meet Nandu

## Slide 2: Purpose
Robotic applications increasingly trend towards closer interaction with humans, thus there is a desire for implementing high force, impedance-controllable end-effectors using cable transmission
Worth exploring nuances of robotic impedance control for cable-driven systems

## Slide 3: Summary
Impedance control end-effector via current control
4-bar linkage gripper geometry
Internal cable-driven gripper transmission, spring return
Actuator: Actuonix P16-P
  12V, 1A (Continuous)
  300N max continuous force
  Potentiometer position feedback
Potentiometer Knob force “setting” control
Trigger-switch engagement

## Slide 4: Control
Actuator closed-loop current feedback control
External pinching force-to-current correlation
Force/current setpoint controlled by user-input potentiometer
Actuator current reading with hall sensor
TMCS1107A4BQDRQ1
Hall Sensor
Actuonix P16-P
(256:1)
TB6612FNG Dual Motor Driver Carrier
Potentiometer
Trigger Switch

## Slide 5: Results
Max Load: 150N Max Pinching Force
Min Load: 10N Min (controllable) pinching force
Impedance Control in gripping action but not releasing action
Difficult to back-drive
  Weak return springs
  Very high internal gear reduction (256:1)
  Relatively high-friction internal leadscrew/nut

## Slide 6: Improvements
Velocity or position control under no-load then switch to impedance control when excess current is sensed
Back-drivable or double-acting mechanism to allow for force control in both gripping and releasing
  Remove the need for return springs that reduce max force output of the gripper